Laser Cutter Instructions:

1. Turn on laser cutter (switch on side)
2. Turn on compressed air (orange nozzle) about ¼ turn clockwise
3. Rest beam focuser (on front of machine) onto laser and press focus on keypad
4. Move focus up and down until it is just touching the material you want to cut
5. For 1/8 inch acrylic press up button 3 to 4 times to focus beam on centre of material
6. Remove focus tool
7. Press reset
8. On computer: click print: properties. Set to 24x18
9. Select vector
10. Set freq to max and set cutting speed to 16?
11. Press OK and print
12. Turn middle valve from 0 to FWD
13. Hit GO on the machine
14. If it doesn’t cut all the way through material, use a slower speed